### STM32F103C8T6 Blue Pill Pin Configuration
Category	Pin Name	Details
Power	3.3V, 5V, GND	3.3V – Regulated output voltage from the onboard regulator (drawing current is not recommended), can also be used to supply the chip. / 5V from USB or onboard regulator can be used to supply the onboard 3.3V regulator. / GND – Ground pins
Analog Pins	PA0 – PA7 / PB0 – PB1	Pins act as ADCs with 12-bit resolution
Input/output pins	PA0 – PA15 / PB0 – PB15 / PC13 – PC15	37 General-purpose I/O pins.
Serial	TX1, RX1 / TX2, RX2 / TX3, RX3	UART with RTS and CTS pins
External interrupts	PA0 – PA15 / PB0 – PB15 / PC13 – PC15	All digital pins have interrupt capability
PWM	PA0 – PA3 / PA6 – PA10 / PB0 - PB1 / PB6 – PB9	15 PWM pins total
SPI	MISO0, MOSI0, SCK0, CS0 / MISO1, MOSI1, SCK1, CS0	2 SPI
Inbuilt LED	PC13	LED to act as a general-purpose GPIO indicator
I2C	SCL1, SDA1 / SCL2, SDA2	Inter-Integrated Circuit communication ports
CAN	CAN0TX, CAN0RX	CAN bus ports